## Slide 1: Scheduling Algorithms

## Slide 2: First-Come, First-Served Scheduling
The process that requests the CPU first is allocated the CPU first. The implementation of the FCFS policy is easily managed with a FIFO queue. When a process enters the ready queue, its PCB (process control block) is linked onto the tail of the queue.
When the CPU is free, it is allocated to the process at the head of the queue. The running process is then removed from the queue. The code for FCFS scheduling is simple to write and understand.
On the negative side, the average waiting time under the FCFS policy is often quite long.
It supports non-preemptive and pre-emptive scheduling algorithm.

## Slide 3: Convoy effect
Convoy Effect is phenomenon associated with the First Come First Serve (FCFS) algorithm, in which the whole Operating System slows down due to few slow processes.
one slow process slows down the performance of the entire set of processes, and leads to wastage of CPU time and other devices
For example: Suppose there is one CPU intensive (large burst time) process in the ready queue, and several other processes with relatively less burst times but are Input/Output (I/O) bound (Need I/O operations frequently) which lead to slow the operating system.

## Slide 4: Disadvantages of FCFS
It is a Non-Preemptive CPU scheduling algorithm, so after the process has been allocated to the CPU, it will never release the CPU until it finishes executing.
The Average Waiting Time is high.
Short processes that are at the back of the queue have to wait for the long process at the front to finish.
Not an ideal technique for time-sharing systems.
Because of its simplicity, FCFS is not very efficient.

## Slide 5: Shortest-Job-First Scheduling
This algorithm associates with each process the length of the process’s next CPU burst. When the CPU is available, it is assigned to the process that has the smallest next CPU burst.
If the next CPU bursts of two processes are the same, FCFS scheduling is used to break the tie.
more appropriate term for this scheduling method would be the shortest-next-CPU-burst algorithm, because scheduling depends on the length of the next CPU burst of a process, rather than its total length . SJN is a non-preemptive algorithm.
This is the best approach to minimize waiting time. It is used in Batch Systems.

## Slide 6: Disadvantages/Cons of SJF
Job completion time must be known earlier, but it is hard to predict.
It is often used in a batch system for long term scheduling.
SJF can't be implemented for CPU scheduling for the short term. It is because there is no specific method to predict the length of the upcoming CPU burst.
This algorithm may cause very long turnaround times or starvation.
Requires knowledge of how long a process or job will run.
It leads to the starvation that does not reduce average turnaround time.
It is hard to know the length of the upcoming CPU request.
Elapsed time should be recorded, that results in more overhead on the processor

## Slide 7: Priority Scheduling
The SJF algorithm is a special case of the general priority-scheduling algorithm. A priority is associated with each process, and the CPU is allocated to the process with the highest priority. Equal-priority processes are scheduled in FCFS order.
An SJF algorithm is simply a priority algorithm where the priority (p) is the inverse of the (predicted) next CPU burst.
The larger the CPU burst, the lower the priority, and vice versa . Priorities are generally indicated by some fixed range of numbers.
Priorities can be defined either internally or externally.
Internally defined priorities use some measurable quantity or quantities to compute the priority of a process. For example, time limits, memory requirements, the number of open files, and the ratio of average I/O burst to average CPU burst have been used in computing priorities.
External priorities are set by criteria outside the operating system, such as the importance of the process, the type and amount of funds being paid for computer use, the department sponsoring the work, and other, often political, factors.
Priority scheduling can be either preemptive or non preemptive
In this type of scheduling algorithm, if a newer process arrives, that is having a higher priority than the currently running process, then the currently running process is preempted.

## Slide 8: Advantages of priority scheduling
Easy to use scheduling method
Processes are executed on the basis of priority so high priority does not need to wait for long which saves time
This method provides a good mechanism where the relative important of each process may be precisely defined.
Suitable for applications with fluctuating time and resource requirements.

## Slide 9: Disadvantages of priority scheduling
If the system eventually crashes, all low priority processes get lost.
If high priority processes take lots of CPU time, then the lower priority processes may starve and will be postponed for an indefinite time.
This scheduling algorithm may leave some low priority processes waiting indefinitely.
A process will be blocked when it is ready to run but has to wait for the CPU because some other process is running currently.
If a new higher priority process keeps on coming in the ready queue, then the process which is in the waiting state may need to wait for a long duration of time

## Slide 10: Round-Robin Scheduling
The round-robin (RR) scheduling algorithm is designed especially for timesharing systems. It is similar to FCFS scheduling, but preemption is added to enable the system to switch between processes.
A small unit of time, called a time quantum or time slice, is defined. A time quantum is generally from 10 to 100 milliseconds in length. The ready queue is treated as a circular queue.
Round Robin is a CPU scheduling algorithm where each process is assigned a fixed time slot in a cyclic way.
It is simple, easy to implement, and starvation-free as all processes get fair share of CPU

## Slide 11: Advantages and disadvantages of rr
Advantages –
  Every process gets an equal share of the CPU.
  RR is cyclic in nature, so there is no starvation.
Disadvantages –
  Setting the quantum too short, increases the overhead and lowers the CPU efficiency, but setting it too long may cause poor response to short processes.
  Average waiting time under the RR policy is often long.

## Slide 12: Multilevel Queue Scheduling
It may happen that processes in the ready queue can be divided into different classes where each class has its own scheduling needs. For example, a common division is a foreground (interactive) process and background (batch) processes. These two classes have different scheduling needs. For this kind of situation Multilevel Queue Scheduling is used.
Ready Queue is divided into separate queues for each class of processes

## Slide 13: example
let us take three different types of process System processes, Interactive processes and Batch Processes. All three process have there own queue . All three different type of processes have there own queue. Each queue have its own Scheduling algorithm. For example, queue 1 and queue 2 uses Round Robin while queue 3 can use FCFS to schedule there processes
Each queue has absolute priority over lower-priority queues

## Slide 14: Multilevel Feedback Queue Scheduling
The multilevel feedback queue scheduling algorithm, in contrast, allows a process to move between queues. The idea is to separate processes according to the characteristics of their CPU bursts.
If a process uses too much CPU time, it will be moved to a lower-priority queue. This scheme leaves I/O-bound and interactive processes in the higher-priority queues.
In addition, a process that waits too long in a lower-priority queue may be moved to a higher-priority queue. This form of aging prevents starvation.

## Slide 15: In general, a multilevel feedback queue scheduler is defined by the following parameters:
• The number of queues
• The scheduling algorithm for each queue
• The method used to determine when to upgrade a process to a higher priority queue
• The method used to determine when to demote a process to a lower priority queue
• The method used to determine which queue a process will enter when that process needs service